MARS I Firmware 	Box	50.23.000
 		DSP	50.18.000

Stand	50.25.000

Release date: 09 november 2016

Below is a list of things that are new and/or changed in this version compared with 
the previous version.
Please note: This version is only compatible with RheoWin 4.63.0003 or newer.

1) The actual lift speed did not correspond to the lift speed values selected in the RheoWin Lift
    element. This has been changed, the actual lift speed now corresponds to the selected value.
    Because the existing selectable lift speed values were relatively low, four new lift speed values
    (5, 10, 20 and 50 mm/s) have been added.

2) The control of axial ramps has been optimized and is now more accurate.

3) The temperature of the Peltier heatsink (of the TM-PE-P and TM-PE-C) is now continuously 
    monitored. When the heatsink temperature reaches an unexpected value (due to insufficient 
    cooling), the Peltier temperature control will be halted and a message will be displayed on the
    instruments control panel.

MARS I Firmware 	Box	50.20.000
 		DSP	50.18.000

Stand	50.24.000

Release date: 03 june 2016

Below is a list of things that are new and/or changed in this version compared with 
the previous version.

Please note: This version is only compatible with RheoWin 4.62.0000 or newer.

Box firmware

1) Improved OSC CD Mode
    The general performance of the deformation (strain) control in oscillation mode (CD-OSC) 
    has been (substantially) improved regarding stability, accuracy, etc.
2) New OSC CD mode with active compliance correction 
    Active compliance correction consists of an active compensation of the compliance of the 
    drive motor + rotor shaft, so that the set deformation value is always achieved. In all 
    previous firmware versions the compliance correction was passive. As long as the 
    deformation is within the linear visco-elastic range, the G’ and G” values resulting from 
    measurements with active and passive compliance correction should be identical.
3) New OSC CS mode with active inertia correction
    Active inertia correction consists of an active compensation of the inertia of the drive motor 
    + rotor shaft, so that the set stress value is always achieved. In all previous firmware 
    versions the inertia correction was passive. As long as the resulting deformation is within 
    the linear visco-elastic range, the G’ and G” values resulting from measurements with active 
    and passive inertia correction should be identical.

MARS I Firmware 	Box	50.17.000
 		DSP	50.17.000

Stand	50.24.000

Release date: 11 april 2016

Below is a list of things that are new and/or changed in this version compared with 
the previous version.

Stand firmware

1) Some modifications were made for compatibility with modified electronics hardware. 
    Firmware version 50.24.000 must be used for all newer MARS I (delivered starting from
    2016), using any older firmware in these instruments will make the instrument inoperative.
    Firmware version 50.24.000 is compatible with any MARS I, that is also with older 
    instruments.

MARS I Firmware 	Box	50.17.000
 	DSP	50.17.000

Stand	50.22.000

Release date: 20 november 2015

Below is a list of things that are new and/or changed in this version compared with 
the previous version.

Stand firmware

1) The gap zero point is now being searched for until the lowest possible position.

MARS I Firmware 	Box	50.17.000
 	DSP	50.17.000

Stand	50.21.000

Release date: 14 july 2015

Below is a list of things that are new and/or changed in this version compared with 
the previous version.

Box & DSP firmware

1) There was a problem with the absolute angle signal during oscillation measurements with f > 1 Hz.
    This has been solved.

2) The quality of the temperature and normal force signals has been improved.

3) The quality of the temperature and gap signals during oscillation measurements has been 
    improved.

4) The Rheonaut Module can now be used together with electrical hood module (TM-EL-H) for 
    improved temperature control at elevated temperatures.

Stand firmware

1) There was a problem with the lift-motor control. This has been solved.
2) The normal force control has been improved.

----------

Contact Thermo Fisher Scientific

If you have any questions and or suggestions regarding the MARS (firmware)

please send an e-mail to:

support.mc.de@thermofisher.com

----------

This file was last updated on: 28.06.2016 by Jint Nijman.